## Slide 1: Claw Arm
Christian Crowley
Yunsik Jung
Matthew Stanley

## Slide 2: Overview
Complex Robotic hands exist in the market
Without nervous system integration they are hard to control
Prosthetics with limited degrees of freedom are still valuable given todays technology
Proposed Gripper that is controlled through pressure

## Slide 3: Requirements
Project Requirements
  Incorporate a Custom PCB
  One Sensor and One Actuator
System Requirements
  Grab an Object
  Detect when Object is Grabbed
  Output Size of the Object

## Slide 4: Mechanical Design
All components 3D printed
One claw is mobile and one is stationary
Rack and Pinion gear set for actuation

## Slide 5: Mechanical Design
Spur Gear | 
Module | 1
Number of teeth | 12
Pitch Circle Diameter | 12 (mm)
External Diameter | 14 (mm)
Rack Gear | 
Module | 1
Height | 2.5 (mm)
Height of end teeth | 0.25 (mm)
Pressure angle | 20
Rack Gear | 
Module | 1
Height | 2.5 (mm)
Height of end teeth | 0.25 (mm)
Pressure angle | 

## Slide 6: Pcb Design

## Slide 7: Sensors and Actuators
Actuator:
  Stepper Motor Motion of the claw
Sensor:
  Two Buttons Control state of claw
  Potentiometer Control brightness of LCD
  Pressure Sensor Measure grip on object

## Slide 8: State Machine
Calibrate
  Finds the closed and opened position for self
Stationary
  Display size of object and waits for instruction
Open
  Opens claw until max distance is reached
Close
  Close until there is pressure on the claw or fully closed

## Slide 9: Distance Calibration

## Slide 10: Questions?